## Slide 1: Introduction to
Jessica “STING” Peterson
Open Matlab while we get started!

## Slide 2: Objectives
Get Matlab working for you here at TPS
  Matlab newbies: Equip you enough to be dangerous
  Matlab wizards: Show you how to use TPS tools for data processing
Demonstrate data analysis tools previously developed
  It is impossible to make you a MATLAB expert in 1.5 hours. The intent of this class is to kick start your learning (or re-learning) of this powerful tool!
Notes: We’re not going to make you a power user or level 9 Matlab Wizard in the next hour and a half. Enough to arm you to work on your own, and to play around with the existing functions that are helpful here at TPS.

## Slide 3: What we’re covering
Initial Setup and Familiarity
Basic Functionality
Tools for using TPS Instrumentation Data
Example Project

## Slide 4: Setup Matlab
Copy folders from “R drive” to → My Documents\MATLAB
  R:\21-B\1.0 - Academics\TF 6510 - Intro to MATLAB\code
Set and save the file path
  Option 1: “Set Path” in HOME tab → “Add with subfolders”→ “Save”
  Option 2: Right click folder → “Add to path”→”Selected folder and subfolders”
    Type “savepath” into console
Open “instructor_example.m” and “Run”
  Familiarize with code, comments, and output figure

## Slide 5: Adding folders to path

## Slide 6: Getting Help!
Help Button
doc “function_name”
help “function_name”
Google “MATLAB _______”
Matlab Central
  Caution!
  You may find answers on the internet that apply to a different version of Matlab!
Pay attention to Matlab version: 2015B vs. 2020A
Notes: Show the various ways to get help on plots.
As of 10 July 2018, searching “Matlab Plots” in Google yields the page shown as the first item.
WRT the Caution – if you search for “Matlab plot multiple y axes,” in the R2015b docsearch you’ll find plotyy as the 8th item on the list, whereas online (R2018) will point you to use yyaxis

## Slide 7: Basic Layout Fam
Moving Windows
Docking/Undocking
Get-well
“Home” tab

## Slide 8: What we’re covering
Initial Setup and Familiarity
Basic Functionality
Tools for using TPS Instrumentation Data
Plotting
Example Project

## Slide 9: Why Matlab?
MATrix LABoratory (MATLAB)
  Fast Matrix Math
  Excel is slow with large quantities of data
  MATLAB easily handles large amounts of raw data
  Powerful Toolboxes for many disciplines
    Statistics, signal processing, control systems, etc…
  Makes programming accessible to the novice user
    Interpolated language – no compiling

## Slide 10: You did finish the MATLAB Academy Module, right?
https://matlabacademy.mathworks.com/
Create an account to access the course.

## Slide 11: Basics Refresher
Variable assignment
  REMINDER - MATLAB does not accept spaces in variable or file names
    Use “_” instead
Data Types
  numeric
  logical
  Character Arrays
  Structures
  Cell Arrays
Demo math functions
  sin(pi/2)
  sqrt(100)
Notes: Functionality discussion – cover arrays & array indexing

## Slide 12: Common Errors – Matrix Math
  Transpose:
Columns separated by “,” or space and Rows separated by “;”
Order and Orientation of Matrix Matters
Tell me ans & why
  A*B →
  A*B’ →
  A’*B →
  A.*B →
Notes: Error (inner dimensions must agree)
32
[4 5 6; 8 10 12; 12 15 18]
[4 10 18]

## Slide 13: More Matrix Fun
Accessing Values in Arrays
  C = [4 5 6; 8 10 12; 12 15 18]
  C(2,1) accesses value in row 2, column 1
  C(2,:) provides all values in row 2
  C(:,2) provides all values in column 2
  How do I get Rows 2 and 3 in Column 1?
  MyText = 'Hello World‘;
  How do I access just the last word?

## Slide 14: Scripts (aka “m” files)
Nothing more than a bunch of commands stored in a file
MATLAB compiles as it executes
Cleanup
  clear all - clears all variables in workspace
  close all - closes all figure windows
  clc - clears the command window screen
  Good to do before new scripts are run
Create new .m file
  Use % at the beginning to make comment lines
  Save script as Example_19B.m
    (Remember, no spaces allowed)

## Slide 15: What we’re covering
Initial Setup and Familiarity
Basic Functionality
Tools for using TPS Instrumentation Data
Plotting
Example Project

## Slide 16: Data
TPS/TS will produce time stamped data in .csv format
  Drop data off with James &/or Jordan

## Slide 17: Importing Data
Several options for loading data
More function call options than shown
  csvread(filename) Only Numerical Values
    (Won’t work w/ TPS DAS data because of the header!)
  xlsread(filename) Only Excel files. (Works w/ *.csv but takes a long time, if it works)
  readtable(filename) Any Data Type
  tpsread(filename) Only Numerical Values
  Manually in Matlab – double click file
  Evil’s TPS_data_norm a real-time view and parser of data
Decide what works best for you
Some may be quicker for automation

## Slide 18: Opening Data
File_name = 'C:\Users\[ID#]\Documents\MATLAB\tps_code\Examples\F-16 Chap 10.csv';
Use TPS read
  data1 = tpsread(File_name);
  data1 is a Structure
    Access the data with “data1.PARAMETER”
    I.e. “plot(data1.IRIG_TIME, data1.MACH)”
  Automatically saved as a “*.mat”
    Only have to “read” one time
…

## Slide 19: Manual Input
Double Click File (from the “current folder”)
Highlight the data you want
“Import Selection”
Now local variables in workspace
Save for reuse as a *.mat file
  Right Click -> Save As

## Slide 20: Evil Bill’s TPS Data Norm
Basic Steps
  Open TPS_data_norm
  Select the data CSV file
  Select the output location
  If you have a lot of events, select the “Create Separate Event Structures”
  Select “Open Quick Data Review Utility” to manipulate data now, if not, you can use TPS_data_utility later
  Click Go
  Select parameters of interest
  Once done, it moves to TPS_data_utility
  Open the file you just created
  Manipulate data with the utility GUI

## Slide 21: Evil Bill’s Data Utility
Data Utility
  EC_### are “Subsets” by event numbers
  Select a new range of data
    Click on the plot for the beginning of your test point and select the left side “Set”
    Click on the plot for the end of your test point and select the right side “Set”
    Type in a name in “New Subset Name” and click “Create New Subset”
    New subset shows up under the dropdown menu
  Save subset as Matlab file
    Click on “Create WS Vectors”
    Select the data of interest
    Go to the Workspace window and right click to save to a .mat file
  See relationship between two parameters
    Select IV for independent variable
    Select DV for dependent variable
    Click “Plot DV = fn(IV)”

## Slide 22: Other Tools
Lots of pre-made scripts available
  ucon.m (unit conversion)
  Pitot_Statics folder (everything pitot statics)
  Statistics folder

## Slide 23: What we’re covering
Initial Setup and Familiarity
Basic Functionality
Tools for using TPS Instrumentation Data
Plotting
Example Project

## Slide 24: Basic Plotting
2D Plotting Examples
  plot(x) Default line plot
  plot(x,'.') Plots data points with markers ('+', 'x', 'o' etc.)
    Combine w/ other modifiers for color (‘r’, ‘g’, ‘b’) & line type (‘:’, ‘-.’, ‘--’)
  plot(time,x,'.') Adds x-axis values to display
  hold on Allows additional traces to current plot
  plot(time(10:50),x(10:50),'r') You can plot subsets (ensure same # of points)
  figure(3) Create additional figure
  plot(time,x,'-.ok','LineWidth',3,'MarkerSize',10,'MarkerFaceColor',[1,0,0])
    You can change the line type, line size, marker size, etc.
Notes: time = Delta_Irig;
x = ALTITUDE;

## Slide 25: Multiple Plots and Saving Figures
Create a new figure
  figure; or figure(2)
Saving figures
  saveas(gcf,'Sample Figure.fig')
    Can re-open in MATLAB and edit
  saveas(gcf,'Sample Figure.png')
    Put it into a report!

## Slide 26: Making prettier plots
Label your axes (more on this in later classes)
  xlabel('Elapsed Time (seconds)','FontSize',14,'FontWeight','bold')
  ylabel('Altitude (feet)','FontSize',14,'FontWeight','bold')
  title('Simple Title','FontSize',18,'FontWeight','bold')
Put data in your titles:
  mn_data = mean(x);
  std_data = std(x);
  title(['My First Plot with \mu = ' num2str(mn_data) ' and \sigma = ' num2str(std_data)]);
Open the editor for more power
Use TPS Title for Flight Test Figs
  bigtitle = 'My First Plot';
  coltext = {{1st Column Array},{2nd Column Array}}
  fonts = [14 11]; ratios = [0.1 0.7];
  tpstitle(bigtitle,coltext,fonts,ratios);
Notes: TPS Title Example
bigtitle = 'My First Fancy Title';
Array1{1,1} = 'Aircraft';Array1{2,1} = 'Date'; Array1{3,1} = ' '; % empty space to allow column lengths to match
Array2{1,1} = 'Fuel Load: xx klbs';Array2{2,1} = 'Maneuver';Array2{3,1} = 'Standard Day';
coltext = {Array1, Array2};
fonts = [14 11]; ratios = [0.1 0.7];
tpstitle(bigtitle,coltext,fonts,ratios);

## Slide 27: Practice / Knowledge Check
Create the following plot:
Data:
  Time span: 0 – 12 months, data intervals of 1 day
  Input: Workload TPS puts on you can be represented by a sine wave of amplitude of 10 work units biased by 15 work units and cycles about once every two weeks (assume 30 day month).
  Output: input multiplied by
Notes: See SHACK for the script showing one way to do this

## Slide 28: What we’re covering
Initial Setup and Familiarity
Basic Functionality
Tools for using TPS Instrumentation Data
Plotting
Example Project

## Slide 29: Example Project
C:\Users\1274642188C\Documents\MATLAB\Instro Data Tools
  Use the data file Example_C12.csv
Pitch Doublet Parameters
  Delta_Irig (time)
  POS_AOA (AoA)
  POS_YOKE_LON (Yoke Position)
  ADC_ALT_29 (Pressure Altitude)
  ADC_IAS (Indicated Airspeed)
Data
  Event #8
Save as example_Phugoid.mat

## Slide 30: Exercise Plot
We are going to plot the Phugoid response:

## Slide 31: Your Turn = “Homework”
.. \Documents\MATLAB\Homework
  Assignment: MATLABHomework_20170725.pdf
  Data File: “Lat_Dir_Data.csv”
Method:
  Your choice

## Slide 32: Additional Resources
.. \ Documents\MATLAB\tps_code\Reference
  Good resources (though most a little dated)
..\Documents\MATLAB\Homework
  Good exercises to get you more familiar with the functionality of MATLAB and the DAS data – NOT GRADED
  We don’t have the time to get to this in class, though we can start (time dependent). It is an optional exercise. I will gladly assist or work these exercises with you off line if desired.
..\Documents\MATLAB\Workshop
  We’ll work this during the remainder of class
  Great opportunity to look at scripts of “fair” complexity and get you spun up looking at data
MATLAB Central (“Community” button)
  http://www.mathworks.com/matlabcentral/fileexchange/

## Slide 33: Backup

## Slide 34: Structures & Cells
Structures
  Helpful for organizing data
    Across numerous flights
    Or test points within a flight
  Define
    x = data.x;
    time = data.Delta_Irig;
    aoa = data.AOA;
Cell Arrays {}
  Can be used to store strings, matrices, etc.
    s = ‘Hello’;
    t = ‘There!’;
    S = {s,t,C} Variable names are case sensitive
  Call back using {}… p = S{2} -> p = There!